## Slide 1: ACLs (Access Control Lists)

## Slide 2: What’s the use?
Security:
Used as a Packet Filter
  Limit network traffic to increase network performance
  Provide traffic flow control
  Provide a basic level of security for network access
  Filter traffic based on traffic type
  Screen hosts to permit or deny access to network service
  Provide priority to certain classes of network traffic

## Slide 3: What we Got
Standard ACLs:
Match based on source IP only
Numbered 1-99 or 1300-1999, Configured in global config mode
Named, Configured with sub commands
Extended ACLs:
Match based on source/destination IP, port, protocol etc.
Numbered 100-199 or 2000-2699,
Named

## Slide 4: Rules of the Road
ACLs:
Must be APPLIED to an interface (inbound or outbound)
Standard ACLs are applied on the CLOSEST router to the Destination
Extended ACLs are applied on the CLOSEST router to the Source
ACLs have an IMPLICIT DENY at the end of every list (aka: If rule is not on the list, then packet is denied/dropped!)
Apply Top to Bottom. If first rule is permit and applies, then the packet is permitted and the other rules are not looked at.
Notes: Inbound-traffic coming to the router
Outbound-traffic leaving the router

## Slide 5: Standard ACL Configuration Commands
Numbered ACL: Access-list # {deny | permit} source ip source wildcard
Ex: Access-list 1 (1-99) deny 1.1.1.1 0.0.0.0 or Access-list 1 permit any
Named ACL: ip access-list standard acL-name
[entry-number] {Deny | Permit} source ip wildcard mask
Ex: IP access-list standard Local_ACL
Permit 172.168.1.0 0.0.0.255
Notes: (let it be know that you can configure the numbered acls through sub commands like the named way

## Slide 6: Extended ACL Configuration Commands
Numbered ACL: Access-list # {deny | permit} protocol source-ip source-wildcard destination-ip destination-wildcard
Ex: Access-list 101 (100-199) deny tcp 1.1.1.1 0.0.0.0 2.2.2.2 0.0.0.0 Ex: Access-list 101 tcp permit any any
Named ACL: ip access-list extended acL-name
[Seq-num] {deny | permit} protocol source-ip source-wildcard destination-ip destination-wildcard

## Slide 7: Extended ACLs Protocols
Use ip if you don’t care about what protocol
Ex: Permit ip any any
If single host address, must use host command
Notes: 1: ICMP
6: TCP
17: UDP
88: EIGRP
89: OSPF

## Slide 8: Common ACL Configuration Commands
Applying an ACL: ip access-group # {in | out}
Ex: ip access-group 1 in
See all access lists: Do show Access-lists
Adding a description for an ACL: Access-list # remark

## Slide 9: Editing ACLs
Numbered ACL way:
Cannot delete ACE with Numbered way, you delete the whole ACL!
Named ACL:
Delete ACE (Access Control Entry) with no entry-number
Command to help edit ACLs: Ip access-list resequence acL-id starting-seq-num increment
Notes: (let it be know that you can configure the numbered acls through sub commands like the named way